## Slide 1: Presented by_ _
Md Aminul Islam - 183002137
Joy Pal - 201002418
Shourav Podder - 202002048

## Slide 2: 8085 Addressing Modes & Memory Mapping

## Slide 3: Content
3
01
02
03
04
Introduction
Types of Addressing modes
Addressing Modes Details
Memory Mapping

## Slide 4: Addressing Modes of 8085
The Way of specifying data to be operated by an instruction is known as addressing modes.
The term addressing mode refers to the way in which the operand of the instruction is specified.
4

## Slide 5: Types of Addressing Modes
8
  1. Immediate Addressing Mode
  2. Direct Addressing Mode
  3. Indirect Addressing Mode
  4. Register Addressing Mode
  5. Implicit Addressing Mode

## Slide 6
5
Immediate Addressing Mode
The operand is specified within the instruction itself.
MOVI B, 45H
Ex-1
Ex-2
LXI B, 45H

## Slide 7
Direct Addressing Mode
The address of the operand is given in the instruction itself.
LDA 502
Ex-1
Ex-2
77H | 88H | 4050 H | 22H | 100H
500 | 501 | 502 | 503 | 504
STA 504

## Slide 8
Indirect Addressing Mode
The address of operand is specified by a register pair.
MOV A, M | Move data from memory location specified by H-L pair to accumulator.
Ex-1

## Slide 9
  Register Addressing Mode
The operand is in general purpose register.
Ex-1
MOV A, B | Move the contents of register B to A.
MOV is the operation.
B is the source of data.
A is the destination.

## Slide 10
  Implicit Addressing Mode
If address of source of data as well as address of destination of result is fixed, then there is no need to give any operand along with the instruction.
CMA | Complement accumulator.
CMA is the operation.
A is the source.
A is the destination.
Ex-1

## Slide 11
Memory Mapping
A15 | A14 | A13 | A12 | A11 | A10 | A9 | A8 | A7 | A6 | A5 | A4 | A3 | A2 | A1 | A0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SA = F000H
EA = F3FF H
It is the process of assigning address range to each memory IC in a microcomputer.
8-bit microprocessor has 16-bit address bus (A0 – A15) with a 1KB memory chip
Example

## Slide 12
Memory Mapping
A13
A14
A15
A10
A11
A12
CS
Decoder
0
7
1 KB *8
RAM
A0-A9
8

## Slide 13
Thank you…